## Slide 1
TEAM 22 · MEMBER 2 SCOPE
Automated Laboratory Camera
Examination Proctoring Framework
Technical Contributions & Targeted Literature Survey
Mahalingam S. | CB.SC.P2CSE26016
Member 2 — System Architecture & Infrastructure Integration
19CSE601 Research Methodology | Dept. of Computer Science & AI

## Slide 2
OVERVIEW
What This Presentation Covers
1
Technical Contributions
Lab camera infrastructure, cheating taxonomy, 7-stage pipeline, risk fusion & explainable AI.
2
Three Targeted Papers
Peer-reviewed studies (2025–2026) that directly back my specific design decisions.
3
Full Literature Survey
13 studies organized across 4 thematic pillars connected to the framework.
4
Comparative Summary
How the proposed framework stacks up against prior proctoring systems.
5
Research Gaps Addressed
Four concrete gaps in existing work that this framework closes.
Team 22 · Member 2 — Mahalingam S.
2

## Slide 3
TECHNICAL CONTRIBUTIONS
Camera Infrastructure & Zero-Cost Deployment
Common Laboratory HD Camera Setup
Engineered the high-precision video processing pipeline leveraging existing overhead CCTV or wide-angle USB cameras already installed in computer labs — interfaced directly to central lab workstations for real-time visual threat monitoring.
Zero-Hardware-Cost Deployment Model
Formulated an institutional deployment architecture that repurposes pre-installed university lab cameras and workstation compute, completely eliminating per-desk hardware procurement expenses.
1080p
VIDEO RESOLUTION
30 FPS
REAL-TIME CAPTURE RATE
$0
ADDITIONAL HARDWARE COST
Team 22 · Member 2 — Mahalingam S.
3

## Slide 4
TECHNICAL CONTRIBUTIONS
4-Class Physical Malpractice Taxonomy
Formulated for computer laboratory examination halls
1
Candidate Impersonation
Unregistered individual seated at candidate station.
FaceNet cosine distance > 0.40
2
Prohibited Electronic Gadgets
Smartphones or smartwatches visible on desk or hands.
Fine-tuned YOLOv8-Nano
3
Unauthorized Notes / Cheat Sheets
Paper slips or unapproved stationery on the desk.
Fine-tuned YOLOv8-Nano
4
Suspicious Head Turning / Glance Sharing
Candidate turning head sideways toward neighboring workstations.
MediaPipe 3D Pose SolvePnP · Yaw > 35°
Team 22 · Member 2 — Mahalingam S.
4

## Slide 5
TECHNICAL CONTRIBUTIONS
7-Stage End-to-End Processing Architecture
1
Frame Acquisition
HD 1080p video stream capture via OpenCV.
→
2
Biometric Identity Verification
128D FaceNet embedding extraction & matching.
→
3
Real-Time Object Inference
Fine-tuned YOLOv8-Nano scans for prohibited gadgets.
→
4
3D Pose & Gaze Tracking
MediaPipe 468 keypoints & SolvePnP Euler angles.
5
Visual Risk Score Aggregation
Calibrated multimodal risk weighting formula.
→
6
Explainable AI (XAI) Generation
Grad-CAM heatmaps & SHAP attributions.
→
7
Dashboard Alerting & Audit Logging
Invigilator UI alerts & timestamped JSON logs.
Team 22 · Member 2 — Mahalingam S.
5

## Slide 6
TECHNICAL CONTRIBUTIONS
Visual Risk Fusion Model & Explainable AI
RiskTotal = 0.40 × AuthRisk + 0.40 × ObjectRisk + 0.20 × PoseRisk
Malpractice Flagged = True if RiskTotal ≥ 0.25 else False
◈
Grad-CAM Saliency Heatmaps
Visual verification of item bounding boxes — shows exactly where the model is looking when it flags an object.
∑
SHAP Additive Attributions
Transparent, per-modality breakdown of the aggregated risk score for full auditability.
Team 22 · Member 2 — Mahalingam S.
6

## Slide 7
PART TWO
Literature Survey
13 peer-reviewed studies (2025–2026) across 4 thematic pillars — grounding every design decision in current research.
Team 22 · Member 2 — Mahalingam S.
7

## Slide 8
LITERATURE SURVEY
Three Papers Directly Backing My Contributions
P1
Smart CCTV Exam Monitoring to Detect and Alert Suspicious Activities Using Deep Transfer Learning
Procedia Computer Science (Elsevier), Vol. 269, 2025
DIRECT CONNECTION
Validates repurposing overhead lab CCTV / USB HD cameras — proves $0 additional-hardware invigilation is achievable.
P2
AI-Powered Real-Time Exam Invigilation Support System Using YOLO and ByteTrack
IEEE Intl. Conf. on Communication Networks & Computing, 2026
DIRECT CONNECTION
Aligns with the 4-class taxonomy (gadgets & unauthorized notes) and validates lightweight YOLO on workstation streams.
P3
A Comprehensive Review of the Changing Landscape of Academic Dishonesty in Automated Proctoring
Discover Education (Springer), Vol. 5, 2026
DIRECT CONNECTION
Provides theoretical backing for the 7-stage pipeline and a taxonomy beyond simple webcam gaze tracking.
Team 22 · Member 2 — Mahalingam S.
8

## Slide 9
LITERATURE SURVEY · PILLAR 1
System Architectures & Systematic Reviews
Malhotra & Chhabra (2026a)
Discover Education (Springer), Vol. 5, 2026
Decade-long systematic review of 80 studies (2014–2024): passive visual recording is inadequate for modern cheating tactics; advocates multi-sensory AI aggregation.
Malhotra & Chhabra (2026b)
Discover Education (Springer), Vol. 5, 2026
Analyzes how AI reshapes malpractice tactics, necessitating adaptive, continuous multi-modal proctoring architectures.
Amal et al. (2026)
IEEE ICoECIT 2026
ProctorPlus: a lightweight proctoring pipeline using YOLOv11 for item/person detection, facial recognition, and gaze tracking.
Pranav et al. (2026)
CCIS (Springer), Vol. 2845, 2026
Examines browser-based monitoring alongside visual oversight in higher-education assessment settings.
Team 22 · Member 2 — Mahalingam S.
9

## Slide 10
LITERATURE SURVEY · PILLAR 2
Object Detection & Evidence Integrity
Wang et al. (2025)
Scientific Reports (Nature), Vol. 15, 2025
Combines YOLOv12 object detection with blockchain storage to create tamper-evident audit logs.
Smart CCTV Monitoring (2025)
Procedia Computer Science, Vol. 269, 2025
Applies deep transfer learning to overhead CCTV streams to classify forbidden student movements.
Mohapatra et al. (2025)
JTIM, Vol. 17, No. 2, 2025
Uses embedded cameras to detect candidate gestures and physical interactions in real time.
Patel et al. (2026)
IEEE CNC 2026
Pairs YOLOv8-Nano with ByteTrack centroid tracking for multi-person tracking and item detection.
Team 22 · Member 2 — Mahalingam S.
10

## Slide 11
LITERATURE SURVEY · PILLARS 3 & 4
Biometric Identity Verification & Explainable AI
PILLAR 3 — BIOMETRIC IDENTITY & EDGE AI
Jack et al. (2026)
Discover AI (Springer), 2026
Evaluates a multi-facet facial recognition model for institutional attendance during examination scenarios.
Kumar et al. (2026)
IEEE Trans. AI, Vol. 7, No. 1, 2026
Demonstrates edge AI processing with local feature attributions to preserve candidate privacy.
PILLAR 4 — EXPLAINABLE AI & ACOUSTIC SENSING
Al-Mansoori et al. (2026)
Computers & Education: AI, Vol. 6, 2026
Integrates Grad-CAM visual heatmaps and SHAP feature attributions into proctoring systems.
Sharma et al. (2026)
IJRASET, Vol. 14, No. 2, 2026
Establishes a multimodal baseline combining YOLOv8, FaceNet, and spectral noise analysis.
Nguyen & Ho (2026)
IEEE Access, Vol. 14, 2026
Applies STFT/MFCC features and YAMNet acoustic embeddings for whisper detection.
Team 22 · Member 2 — Mahalingam S.
11

## Slide 12
LITERATURE SURVEY
Comparative Literature Summary Matrix
Research Study
Year
Camera Source
Detection Engine
Hardware Cost
Explainable AI
ProctorPlus (Amal et al.)
2026
Webcam
YOLOv11 + Dlib
High (Per-Student PC)
No
Wang et al. (Nature Sci. Rep.)
2025
Overhead CCTV
YOLOv12 + Blockchain
Medium (Servers)
No
Mohapatra et al. (JTIM)
2025
Desk Embedded Cam
Haar Cascade
$35 / Desk
No
Smart CCTV (Procedia CS)
2025
Overhead CCTV
Deep Transfer Learning
Low
No
Team 22 Proposed Framework
2026
Common Lab HD Camera
FaceNet + YOLOv8 + MediaPipe
$0 (Zero Cost)
Yes (Grad-CAM & SHAP)
Team 22 · Member 2 — Mahalingam S.
12

## Slide 13
LITERATURE SURVEY
Critical Research Gaps Addressed
G1
High Infrastructure & Procurement Costs
GAP
Prior works require dedicated desk cameras or microcontrollers ($35–$100/desk).
ADDRESSED BY
Repurposes pre-installed Lab HD cameras — $0 additional cost.
G2
Network Latency & Resolution Bottlenecks
GAP
Low-power desk micro-chips suffer bandwidth drops and 320×240 video quality.
ADDRESSED BY
Direct USB/Ethernet 1080p @ 30 FPS streams.
G3
Black-Box, Unexplainable AI Flagging
GAP
Traditional deep learning proctoring outputs binary alerts without proof.
ADDRESSED BY
Grad-CAM saliency heatmaps + SHAP additive attributions.
G4
Uncalibrated Single-Modality Risk
GAP
Isolated module detection causes high false-positive rates.
ADDRESSED BY
Calibrated fusion: 0.40 Auth + 0.40 Object + 0.20 Pose.
Team 22 · Member 2 — Mahalingam S.
13

## Slide 14
Thank You
Questions & Discussion
Mahalingam S. | CB.SC.P2CSE26016
Team 22 — Member 2, System Architecture & Infrastructure Integration